## Slide 1
ENERGY AND ENVIORNMENT INTERACTIONS II part

## Slide 2
NUCLEAR ENERGY

## Slide 3: NUCLEAR ENERGY
Synonymous with atomic energy
The nucleus of an atom is the source of nuclear energy.
When the nucleus splits (fission), nuclear energy is released in the form of heat energy and light energy.
Nuclear energy is also released when nuclei collide at high speeds and join (fuse).

## Slide 4: FISSION
Fission occurs when an atom’s nucleus splits apart to form two or more different atoms.
The most easily fissionable elements are the isotopes of U 235 and Pu 239.
When fissionable elements are flooded with neutrons causing the elements to split, they form new radioactive elements and release extra neutrons that create a chain reaction if more fissionable material is present.
While Uranium, atomic number 92, is the heaviest naturally occurring element, many other elements can be made by adding protons and neutrons with particle accelerators or nuclear reactors.
In general, the fission process uses higher atomic numbered elements.
Notes: U: Uranium, Pu: Plutonium

## Slide 5: FUSION
Fusion is the combining of one or more atoms usually isotopes of hydrogen, which are deuterium and tritium.
Atoms naturally repel each other so fusion is easiest with these lightest atoms.
To force the atoms together it takes extreme pressure and temperature, this can be produced by a fission reaction.
The sun’s energy is produced from a nuclear fusion reaction in which hydrogen nuclei fuse to form helium nuclei.

## Slide 6: BRIEF HISTORY
Nuclear energy was first discovered in 1934 by Enrico Fermi.
The first nuclear bombs were built in 1945 as a result of the infamous Manhattan Project.
The first plutonium bomb, code-named Trinity, was detonated on July 16, 1945 in New Mexico, USA.
On August 6th 1945, the first uranium bomb was detonated over Hiroshima. Three days later a plutonium bomb was dropped on Nagasaki. There are over 200,000 deaths associated with these detonations.
Electricity wasn’t produced with nuclear energy until 1951.

## Slide 7
CHICAGO PILE 1, DECEMBER 2, 1942
FIRST SUCESSFUL NUCLEAR REACTOR

## Slide 8
Fossil Fuel (Coal) Energy Density: 2.9 x 107 J/kg
Fuel Consumed by 1000-MWe Plant: 7,300,000 kg/day
Global Coal Consumption: 6.8 billion tons
1 eV = 1.6 x10-19 J
ENERGY FROM FOSSIL FUELS

## Slide 9
Fission Fuel Energy Density: 8.2 x 1013 J/kg
Fuel Consumed by 1000-MWe Plant: 3.2 kg/day
ENERGY FROM NUCLEAR FISSION

## Slide 10
Fusion Fuel Energy Density: 3.4 x 1014 J/kg
Fuel Consumed by 1000-MWe Plant: 0.6 kg/day
ENERGY FROM NUCLEAR FUSION

## Slide 11
Neutrons are emitted when 235U undergoes fission
These neutrons are then available to trigger fission in other nuclei and the process repeats.
If the process is controlled it is termed as chain reaction and used for nuclear power
if uncontrolled, a violent explosion occurs (used for nuclear weapons, 1 g of 235U can release energy equal to 15 Tonnes of TNT)
Nitroglycerine-Dynamite? Alfred Nobel
CHAIN REACTION

## Slide 12
E = mc2

## Slide 13: Fission Reactors
Splitting of U235 by neutron bombardment
  Reaction produces neutrons, fission fragments and heat.
  Starts a chain reaction
U-238 does not undergo fission
Natural Uranium contains U235 (0.72%) and U238(99.28%)
Steam produced runs a turbine coupled with alternator to generate electricity
  Similar to coal/oil/gas burning power plants

## Slide 14
The furnace in which the controlled fission of nuclear fuel takes place is called reactor or atomic reactor.
Fuel elements consist of enriched 235U (natural uranium contains 0.72% 235U and 99.28% 238U)
238U never undergoes fission
Control rods absorb the neutrons
Moderator material helps to slow down the neutrons
BASIC REACTOR DESIGN

## Slide 15
NUCLEAR FISSION REACTOR

## Slide 16
Uranium mines and mills produce radioactive waste material that can pollute the environment
U-235 enrichment and fabrication of fuel assemblies also produces waste materials.
Site selection and construction controversial.
Power plants also the site of past accidents or partial meltdowns.
Handling and disposal of waste
Decommissioning expensive
Terrorists could collect plutonium for bomb
Problems with Nuclear Power

## Slide 17
Nuclear Power Plant Accidents

## Slide 18
Occurred on March 28, 1979 near Harrisburg, PA
  Malfunction of a valve resulted in partial core meltdown
  Intense radiation released to interior of containment structure
  Small amount of radiation released into environment
  Because long-term chronic effects of exposure to low levels of radiation are not well understood, the effects of TMI difficult to estimate.
  Major impact of the incident was fear.
Three Mile Island

## Slide 19
Occurred on April 26, 1986
  Worst accident in history of nuclear power generation
Failure in cooling waters
  Reactor overheated melting the uranium fuel
  Explosions removed top of building
  Fires produced a cloud of radioactive particles
  30 km zone surrounding Chernobyl evacuated
  City of Prypyat, pop. 48,000 at time of accident, now a ghost city.
  Thyroid cancer increased in Belarus, Ukraine and the Russian Federation
  Trees and vegetation damaged
  Ultimately responsible for 16,000 deaths
Chernobyl

## Slide 20
Occurred on March 11, 2011
  Second Worst accident in history of nuclear power generation
Failure in cooling water supply due to tsunami
  Three reactor overheated
  Hydrogen-air explosion
  37 were injured mildly
  2 taken to hospital for serious injuries
  No casualty
  Loss of the power plant
Fukushima Daiichi

## Slide 21
Advocates argue that nuclear power is good for the environment
  It does not produce potential global warming through release of carbon dioxide.
  It does not cause acid rain.
  If breeder reactors are developed the amount of fuel (Thorium- India got maximum reserves) will be greatly increased.
Arguments for standardization
  Safer and smaller plants to provide more energy
Future of Nuclear Energy

## Slide 22
Argument against
  Based on political and economic consideration
  Uncertainty of safety issues
  Known reserves would be used up quickly
  May be a path to nuclear weapons
Future of Nuclear Energy

## Slide 23
FUSION

## Slide 24
All stars generate energy through fusion
The Sun, along with about 90% of other stars, fuses hydrogen
    Some “older” stars fuse heavier elements
Two conditions must be met before fusion can occur in a star
    The temperature must be high enough
    The density of the nuclei must be high enough to ensure a high rate of collisions
FUSION IN NATURE

## Slide 25
Energy releasing fusion reactions are called thermonuclear fusion reactions or simply thermonuclear reactions.
A great deal of effort is being directed at developing sustained and controlled thermonuclear reactions.
A thermonuclear reactor that can deliver a net power output over a reasonable time interval is not yet a reality.
FUSION REACTORS

## Slide 26
India is a quickly advancing an active nuclear power program.
It is expected to have 20 GW of nuclear capacity by 2020, though they currently stand as the 9th in the world in terms of nuclear capacity.
ATOMIC POWER AND INDIA

## Slide 27
Currently, twenty-one nuclear power reactors have a total install capacity of 5,780 MW
Power station | Operator | State | Type | Units | Total capacity (MW)
Kaiga | NPCIL | Karnataka | PHWR | 220 x 4 | 880
Kakrapar | NPCIL | Gujarat | PHWR | 220 x 2 | 440
Madras | NPCIL | Tamil Nadu | PHWR | 220 x 2 | 440
Narora | NPCIL | Uttar Pradesh | PHWR | 220 x 2 | 440
Rajasthan | NPCIL | Kota Rajasthan | PHWR | 100 x 1 200 x 1 220 x 4 | 1180
Tarapur | NPCIL | Maharashtra | BWR PHWR | 160 x 2 540 x 2 | 1440
Kudankulam | NPCIL | Tamil Nadu | VVER-1000 | 1000 x 1 | 1000
 |  |  | Total | 21 | 5780

## Slide 28
Projects under construction
Power station | Operator | State | Type | Units | Total capacity (MW) | Expected Commercial Operation
Madras | Bhavini | Tamil Nadu | PFBR | 500 x 1 | 500 | March 2015
Kakrapar Unit 3 and 4 | NPCIL | Gujarat | PHWR | 700 x 2 | 1400 | Unit 3: June 2015, Unit 4: December 2015
Rajasthan Unit 7 and 8 | NPCIL | Rajasthan | PHWR | 700 x 2 | 1400 | Unit 7: June 2016, Unit 8: December 2016
Kudankulam Unit 2 | NPCIL | Tamil Nadu | VVER-1000 | 1000 x 1 | 1000 | May 2015
 |  |  | Total | 6 | 4300 | 

## Slide 29
Proposed Projects
Power station | Operator | State | Type | Units | Total capacity (MW)
Gorakhpur | NPCIL | Haryana | PHWR | 630 x 4 | 2,800
Chutka | NPCIL | Madhya Pradesh | PHWR | 700 x 2 | 1400
Mahi Banswara | NPCIL | Rajasthan | PHWR | 700 x 2 | 1400
Kaiga | NPCIL | Karnataka | PHWR | 700 x 2 | 1400
Madras | NPCIL | Tamil Nadu | FBR | 500 x 2 | 1000
Site to be decided |  |  | AHWR | 300 x 1 | 300
Kudankulam |  | Tamil Nadu | VVER-1000 | 1000 x 2 | 2000
Jaitapur |  | Maharashtra | EPR | 1650 x 6 | 9900
Kovvada |  | Andhra Pradesh | ESBWR | 1594 x 6 | 9564
Mithi Virdi (Viradi) |  | Gujarat | AP1000 | 1100 x 6 | 6600
 |  |  | Total | 33 | 33564

## Slide 30
NARORA ATOMIC POWER STATION, UNITS 1 & 2, 220 MW EACH

## Slide 31
RAJASTHAN ATOMIC POWER STATION, UNITS 3 & 4, 220 MW EACH

## Slide 32
(P/H)
Example 1
A thermal power plant of 2000 MW capacity is using coal having a heating value of 28.65 MJ/kg. Determine the amount of the coal in tonnes being used by this plant on an annual basis assuming that the plant runs for 325 days in a year and overall conversion efficiency of the plant is 34.56%.
If the above plant is polluting the environment and a decision is taken to replace it with an atomic power plant of the same capacity. Determine the mass of U235 fuel rods required annually to run this plant. U235 fuel rods comprise of 95.55% of U238. This plant may be assumed to run for 325 days in a year with an thermal energy conversion into electricity to be 45.54%.

## Slide 33
SOLAR ENERGY

## Slide 34: SUN
Energy received from the sun in 30 days exceeds total energy available in fossil fuels

## Slide 35
Sun is the only source of all renewable energy
SOLAR ENERGY

## Slide 36
Energy from the sun reaches earth’s surface in the form of solar radiation.
The Sun is a sphere of intensely hot gaseous matter, continuously generating heat by thermo-nuclear fusion reactions, which convert hydrogen atoms to helium atoms.
This energy radiated from the sun in all directions and a very small fraction of its reaches the earth.
The maximum intensity of solar radiation known as solar constant which is defined as the total energy received from the sun, per unit time on a surface of unit area kept perpendicular to the radiation, in space, just outside the earth’s atmosphere when the earth is at its mean distance from the sun. The value of solar constant is 1366 W/m2.
SOLAR RADIATION

## Slide 37
DIFFERENT COLORS OF LIGHT HAVE DIFFERENT WAVELENGTHS AND DIFFERENT ENERGIES

## Slide 38
The Earth receives at an average of 1366 W/m2 energy in the form of electromagnetic radiation from the Sun
This is equivalent to over 43 thousand times the entire power generation rate on the Earth
But…
  Large portion of this energy is absorbed in the atmosphere.
  Not available all the time at one particular place.
  Needs to be collected (absorbed) before its utilization.
SOLAR RESOURCES

## Slide 39
Solar energy is used in three different ways:
By converting solar energy to thermal energy through solar heater (thermal conversion)
By direct conversion of solar energy to electricity through photovoltaic (PV) approach – Most important
By converting solar energy to chemical energy (photosynthesis)
TECHNIQUES FOR USING SOLAR ENERGY

## Slide 40: SOLAR ENERGY CONVERSION
To use solar energy, some part of the electromagnetic spectrum must be converted into two other farms:
  Heat (Thermal Energy)
  Electricity
The amount of heat or electricity produced depends upon the technology used and its efficiency.

## Slide 41: ADVANTAGES AND DISADVANTAGES
Advantages
      All chemical and radioactive pollutants of the thermonuclear reactions remain behind on the Sun, while only pure radiant energy reaches the Earth.
      Energy reaching the earth is incredible. By one calculation, 30 days of sunshine striking the Earth have the energy equivalent of the total of all the planet’s fossil fuels, both used and unused!
Disadvantages
      Solar energy is not available round the clock.
      Available Solar energy is diffused. Required to be focused at one point before using (particularly for thermal conversion).
      Three step approach is required:
      1) collection, 2) conversion, 3) storage.

## Slide 42: SOLAR THERMAL TECHNOLOGIES
Solar thermal is the oldest solar energy technology – has been used for centuries
Solar thermal technologies can be divided in three types:
  Passive solar building design- Our Main building
  Thermal collectors for water heating, space heating and other uses
  Solar thermal power plants-similar to coal/gas based plants

## Slide 43: PASSIVE SOLAR DESIGN
  Passive solar design is a set of practices that accommodate the local climate by:
    Letting the sun into the building in the winter
    Keeping the sun out in the summer
  The most important aspects of passive solar design are
    Building and window orientation
    Insulation and building materials
    Shading

## Slide 44
                A flat-plate collector is used to absorb the sun’s energy to heat (mostly water).
                Two methods of heating: passive (no moving parts) and active (using pumps).
In passive collectors water circulates throughout the closed system due to convection currents.
Tanks of hot water (insulated) are used for storage.
  FLAT PLATE COLLECTOR (CLASSICAL DESIGN)

## Slide 45
Flat-plate solar collector absorbs sunlight and transfer the heat to water or a mixture of anti-freeze (ethylene glycol) and water
The hot fluid can be used directly or indirectly for hot water and space heating
Generally used for low temperature applications like residential hot water heating
  FLAT PLATE COLLECTORS (contd…)

## Slide 46
Evacuated tube collectors use a “thermos bottle” type of collector that prevent freezing and can achieve higher temperatures
Used when large volumes high temperature water are needed like commercial laundries, hotels and hospitals
EVACUATED TUBE SOLAR THERMAL COLLECTORS

## Slide 47
Active System uses antifreeze so that the liquid does not freeze if outside temperature drops below freezing point.
HEATING WATER: ACTIVE SYSTEM

## Slide 48
Photovoltaic cells are capable of directly converting sunlight into electricity.
A simple wafer of silicon with wires attached to the layers. Current is produced based on types of semiconductor (n- and p-types) used for the layers. Each cell produces 0.5 V.
Battery may be needed to store electrical energy or may be connected to grid directly through inverters.
No moving parts, no pollution, do not wear out, but because they are exposed to the weather, their lifespan is about 25 years.
DIRECT CONVERSION INTO ELECTRICITY

## Slide 49
The PV effect was discovered in 19th century by Alexander Becquerel
Bell labs pioneered early application, especially for satellites, in the 1960s
Very small, remote applications emerged in the 1970s and early 1980s
As cost declined, PV became more common for larger applications in late 1980s and early 1990s and now commercial usage has started world over.
PHOTOVOLTAIC TECHNOLOGY - BACKGROUND

## Slide 50
PV CELL MATERIALS
The most common PV cells are made from crystalline silicon wafers
Other types of materials include thin films like Cadmium Telluride (CdTe), Copper-Indium-Gallium-Diselenide (CIGS), amorphous silicon (a-Si)
The main goals for manufacturers are to minimize the amount of materials and maximize efficiency
Today, the best crystalline silicon cells are about 15% efficient, the best thin films are about 8% efficient.

## Slide 51: Mechanism of generation
+
+
+
+
-
-
-
-
Electrode
P-Type Semiconductor
N-Type Semiconductor
Reflect-Proof Film
Electrode
Solar Energy
Load
Electric Current
The solar cell is composed of a P-type semiconductor and an N-type semiconductor. Solar light hitting the cell produces two types of electrons, negatively and positively charged electrons in the semiconductors.
Negatively charged (-) electrons gather around the N-type semiconductor while positively charged (+) electrons gather around the P-type semiconductor. When you connect loads such as a light bulb, electric current flows between the two electrodes.
Notes: I will introduce the principle to begin with.
Solar cell, invented in the USA in 1954, is a kind of semiconductor to convert energy of light directly into electricity. Most semiconductor used for solar cell are silicon semiconductors and it is composed of P-type semiconductor and N-type semiconductor.
Sunlight hitting the cell produces two types of electrons, negatively charged and positively charged electrons in the semiconductors. Negatively charged electrons gather around N-type semiconductor while positively charged electrons gather around P-type semiconductor.
When youconnect loads such as a light bulb or motor, electric current occurs between two electrodes.

## Slide 52: Common types of PV cell
Crystal cell (Single crystal and Poly crystalline Silicon)
Single crystal
Poly crystalline
Formed by melting high purity silicon like as Integrated Circuit
For mass production, cell is sliced from roughly crystallized ingot.

## Slide 53
(P/H)

## Slide 54
GREEN ENERGY
GENERATION@IIT ROORKEE

## Slide 55
SPV Power Plants/units
Solar Water Heating
Solar Heating of Swimming Pool
Solar Steam Cooking
GREEN ENERGY GENERATION
Notes: The various applications that our project proposes are: ***************
Here, we would like to point out that our project does not occupy any ground space of the campus which is precious

## Slide 56: Solar Photovoltaic Electricity Roof top
Cumulative capacity | 1.819 MWp
Roof area covered | 22,000 sq m (27 buildings of all departments and units)
Technology Used | Polycrystalline Silicon
Cost of the system | Rs. 14.14 crore
First 5 year O&M cost | Rs. 13.75 lacs
O&M cost 6 to 25th year | Rs. 3.49 to 15.55 lacs per year
Unit Generation cost | Rs. 8.5 (without subsidy) Rs. 0.85 (with subsidy)
Electricity generation | 30.8 lac units annual
CO2 Reduction | 2464 ton p.a.
Contractor including O&M | Tata Power Solar
Order status | Order placed in Aug, 2013 and installation started
Date of completion | March, 2014
  Global best German make string inverters
  Environment monitoring system for recording parameters like Solar Radiation, Temperature and Wind speed.
  SCADA (supervisory control and data acquisition) system with real-time LCD display of generation at all 27 sites.
Performance Guarantee
  Generation shortfall beyond 10% of guaranteed is liquidated damage equivalent to twice of prevailing tariff.

## Slide 57: Solar Water Heating Systems
Cumulative capacity | 3.4 lacs Litres per day
Cumulative collector area | 6,794 sq. m
No. of buildings | 12 hostels, 2 guest houses 12 residential areas covering all staff
Technology | Evacuated Tube Collector
Electricity savings | 53.71 lac units per annum
CO2 Reduction | 4297 ton per annum
Current status | Working Suppliers: Tata Solar Power
  Storage tank thickness more than standard for extended life.
  No electrical backup, purely solar based.
  Flow-meters and Temperature sensors with SCADA and LCD display
  Separate Storage tank for each group of bathrooms to allow proportionate draining of water.
  Performance Guarantee
  Shortfall of beyond 10% of guaranteed temperature of 60 degree Celsius shall be liquidated damages

## Slide 58
Solar steam cooking
Cumulative collector area | 976 sq. m (using 61 collectors)
No. of buildings | 9 hostel mess
Technology Used | Dish type parabolic solar concentrator
Cost of the system | Rs. 2.14 crore including steam cooking vessels
First 5 year O&M cost | Rs. 45,95,528
LPG savings | Approx 5,000 cylinders(14.2 kg) per year
CO2 Reduction | 234 ton per year
EPC Contractor | Taylormade Solutions
Status | Order placed in Oct, 2013
Completion date | April, 2014
  Rice, Dal, Vegetables for about 5500 students
  Steam at 10 bar pressure
  Single axis automatic sun tracking parabolic dishes of 16 sq. m. area
  Automatic switching system to LPG based backup on cloudy days
  SCADA system for real time monitoring and data acquisition
  LCD display showing all parameters
Notes: The salient features of this system are that:
This system can be used to cook rice, dal ,vegetables…..
Images

## Slide 59
PARTICIPATION WITH STUDENTS
Students involved at all stages including:
  Surveys
  Measurements
  Preparation of designs, drawings, estimates and DPRs
  Strategies for implementation to create ownership, participation and awareness
Future leadership in green initiatives

## Slide 60
(P/H)
Example 1
A flat plate solar thermal collector is installed on the roof of a hotel. The collection surface is 10 m2. Determine the following:
(i) Power collection by surface at 11 AM, if sun insolation is 0.725 kW/m2.
Power collection: 0.725*10= 7.25 kW
(ii) The water tank of the above collector contains 1200 kg of water, initially at a temperature of 34 0C. What will be the temperature of water after 1 hour, assuming constant power collection as in (i) and 65% all the collected energy is being transferred to water.
Total energy in one hr = 7.25*60*60*0.65 kJ=16,965 kJ
By heat balance Q= M Cp delta T
Delta T= 16,965/1200/4.18= 3.38
Final Temperature of water after 1 hr: 34+3.38= 37.38 oC

## Slide 61
Biomass Energy

## Slide 62
What is it?
  Biomass energy is the use of living and recently dead biological material as an energy source
  Ultimately dependent on the capture of solar energy and conversion to a chemical (carbohydrate) fuel
  Theoretically it is a carbon neutral and renewable source of energy
How does work?
  Traditional: forest management, using wood as fuel
  Use of biodegradable waste
    Examples: animal dung, crop residue, sewage, municipal solid waste
  Recent interest in agricultural production of energy crops
    Examples: corn, sugarcane etc.
    Does not have to be a food crop
    Recent interest in bioengineered (GM) plants as fuel sources
  Production of a liquid or gaseous biofuel
    Biogas due to the breakdown of biomass in the absence of O2
      Includes capture of landfill methane
    Bioethanol from fermentation-sugarcane juice, molasses, corn, cellulosic materials
    Biodiesel from nonedible oils and fats
Biomass Energy

## Slide 63
Carbon neutral
  CO2 ultimately released in energy generation is recaptured and so ideally does not change total atmospheric levels
  Sequestration in soil can result in a net decrease in CO2 levels
Biomass Energy

## Slide 64
Advantages
  Versatile
  Renewable
  No net CO2 emissions (ideally)
  Emits less SO2 and NOx than fossil fuels
Disadvantages
  Low energy density/yield
    In some cases (eg, corn-derived bioethanol) may yield no net energy
  Land conversion
    Biodiversity loss
    Possible decrease in agricultural food productivity
  Usual problems associated with intensive agriculture
    Nutrient pollution
    Soil depletion
    Soil erosion
    Ground water contamination
Biomass Energy

## Slide 65
(P/H)
From annual report of MNRE, 2016-17

## Slide 66
(P/H)
From annual report of MNRE, 2016-17

## Slide 67
(P/H)
77 grams of glucose was allowed to ferment to form ethanol and carbon dioxide. 23.4 grams of ethanol was recovered by distillation. Determine the following:
1.What is the theoretical yield of ethanol production from glucose?
2.What is the actual yield from the experiment?
Example 1
Look ?
Is there any usage of CO2 evolving in fermentation process?

## Slide 68: CONCLUDING REMARKS/ ISSUES AFFECTING FUTURE DEVELOPMENT IN ENERGY SECTOR
Population & Urbanization (Developing Countries) | Stress on natural resources, lack in adequate sanitary facilities, and drainage systems, air pollution and water pollution
Health | Toxic pollutants, Impact on human health
Water Scarcity | Water Stress when water supply <1700m3/person-year Water Scarce when water supply <1000m3/person-year
Energy and Climate; Energy consumption has increased in past thirty years and projected to increase in future | Green house gas emissions, climate change, fossil fuel depletion, Increase in temperature in the next centaury: 2.4 to 6.4 0C (IPCC))
Toxic Chemicals and Finite resources (non-renewable & renewable resources) | Problems associated with persistent organic pollution, trace organics (pesticides, pharmaceuticals, personal care products, endocrine disruptors)
Built Environment (buildings, roads, bridges) | High requirement of water, energy and other resources (cement, sand, clay, aggregate, steel, wood etc.)